Cruise Report

Bivalve Larvae TRANSPORT Mapping Survey

Cruise: BT-12-06

Date: June, 19, 2012

Vessel: R/V Terrapin

Area of Operations: Choptank River

Scientific Personnel: Tom Wazniak (Captain), Jake Goodwin (Chief Sci), Jason Spires,

Weather: Overcast, (87 F)

Objectives:

The objectives of this cruise were to 1) determine the physical and biological conditions that cue oyster (Crassostrea virginica) spawning in the Choptank River, and 2) map the distribution of multiple species of bivalve larvae along the salinity gradient and at different depths in the water column.

Activities:

15 stations were occupied where samples were successfully collected (Fig. 1, Table 1). A list of station numbers, names and locations for the Transport program can be found in Table 2.

Overall, 15 CTD casts were made, 28plankton samples were collected, and 8 water samples for chl-a pigment and TSS were collected and delivered to Analytical Services.    Stations were sampled from the mouth of the river to upstream locations.

A CTD cast was made at each station, and the downcast was used to measure water properties. The CTD equipped with a fluorometer, OBS, dissolved oxygen and PAR sensors. Using  hoses attached to the CTD frame, bivalve larvae were collected from near bottom to the surface by moving the CTD up through the water column in 0.5 m depth intervals at regularly spaced time intervals (e.g., every 20 s or every 60 s) depending upon the depth of the station. We estimated that our pumps (50 feet of hose, an in-line flow meter) was pumping at 10 gallons per minute. The water was pumped into a 55-gallon drum half filled with water (to minimize damage to the samples) and through a 64 μm mesh net to collect bivalve larvae. Samples were concentrated and washed with seawater into jars containing 4% buffered formaldehyde.

Water samples were collected for chl-a pigment (using a syringe/filter apparatus) to calibrate the fluorometer and for total suspended solids (using a water bottle provided by Analytical Services) to calibrate the OBS (Table 3).

Summary:

Cruise BT-12-06 was successful.  3 bottom pycnoclines were observed, four oblique samples were taken.

Table 1. Consecutive station log

Table 2. Station numbers, names and locations for the TRANSPORT program.

Table 3. Water Sample Logs for cruise BT-12-06

Fig. 1 Sampling locations (TRANSPORT stations) in the Choptank River for cruise 12-06

# Text boxes

Harris Creek 2

8.0

-76.3122

38.7141

076º 18' 44" W

38º 42' 51" N

21

Harris Creek 1

5.0

-76.3040

38.7360

076º 18' 14" W

38º 44' 10" N

20

Cabin Creek

4.0

-75.9791

38.6367

075º 58' 45" W

38º 38' 12" N

15

Jamaica Pt

12.0

-75.9831

38.6057

075º 58' 59" W

38º 36' 20" N

14

Oystershell Pt

7.5

-76.0102

38.5884

076º 00' 37" W

38º 35' 18" N

13

Bolingbroke Sands

4.5

-76.0424

38.5761

076º 02' 33" W

38º 34' 34" N

12

Choptank Bridge

8.5

-76.0580

38.5801

076º 03' 29" W

38º 34' 48" N

11

Hambrooks Bar

13.0

-76.0838

38.5991

076º 05' 02" W

38º 35' 57" N

10

Jenkins Creek

5.0

-76.1121

38.5938

076º 06' 44" W

38º 35' 38" N

09

Martin Pt

11.0

-76.1328

38.6297

076º 07' 58" W

38º 37' 47" N

08

Bachelor Pt

5.5

-76.1830

38.6679

076º 10' 59" W

38º 40' 04" N

07

Castle Haven Pt

10.0

-76.1974

38.6400

076º 11' 51" W

38º 38' 24" N

06

Benoni Pt

4.5

-76.2176

38.6736

076º 13' 03" W

38º 40' 25" N

05

Broad Creek

6.5

-76.2604

38.7149

076º 15' 38" W

38º 42' 54" N

04

near Tilghman

6.0

-76.2826

38.6876

076º 16' 57" W

38º 41' 15" N

03

near buoy R12

9.0

-76.2747

38.6501

076º 16' 29" W

38º 39' 00" N

02

Choptank Mouth

11.0

-76.3273

38.6361

076º 19' 38" W

38º 38' 10" N

01

Location

Depth (m)

Decimal Lon

Decimal Lat

Longitude

Latitude

Station